## Slide 1
1.1 OVERVIEW OF PROGRAMMABLE CONTROLS
Lesson 1: PROGRAMMABLE CONTROLS

## Slide 2
After completing this lesson, learners will be able to:
Speech on the concept of programmable control.
Compare the pros and cons of programmable control with other forms of control.
Present the applications of PLC in practice.
LESSON OBJECTIVES
INS3150 - PROGRAMMING PLC

## Slide 3
Control overview.
Applications of PLC in real life.
Hardwired control and programmable control.
Compare PLC with other controls.
3
INS3150 - PROGRAMMING PLC
1.1 OVERVIEW OF PROGRAMMABLE CONTROLS

## Slide 4
In the field of control, two control methods are distinguished: + Hard-connected control method. + Programmable control method.
Nowadays, the requirements for automation in industry are increasing, requiring many changes in control techniques in terms of equipment as well as control methods.
1.1 OVERVIEW OF PROGRAMMABLE CONTROLS
INS3150 - PROGRAMMING PLC

## Slide 5: MECHANICAL CONTROLS
+ Non-contact hardfacing control: Using logic gates, digital ICs, sensors, etc. Power components such as SCR, TRIAC.
+ Contact-based hard-connected controls: Using electromagnetic instruments such as relays, contactors, sensors, etc. These instruments are connected together according to specific circuits.
1.1 OVERVIEW OF PROGRAMMABLE CONTROLS
INS3150 - PROGRAMMING PLC

## Slide 6
Define technology requirements
Control scheme design
Selecting Circuit Elements
Circuitry, bonding of elements
Test Run - Circuit Test
HARDWIRING CONTROL STEPS
1.1 OVERVIEW OF PROGRAMMABLE CONTROLS
INS3150 - PROGRAMMING PLC

## Slide 7






K1
K2
Off
ON
Rth1
Rth2
K1
K1






K3
K2
Off
ON
Rth1
Rth2
K3
K3
EXAMPLE 1
The two motor run sequentially
Two motors sequential stops
1.1 OVERVIEW OF PROGRAMMABLE CONTROLS
INS3150 - PROGRAMMING PLC

## Slide 8
Two motors run sequentially, stop sequentially






K1
RT
Off
ON
Rth1
K1
K1


K2
Rth2
RT
EXAMPLE 2
1.1 OVERVIEW OF PROGRAMMABLE CONTROLS
INS3150 - PROGRAMMING PLC

## Slide 9: PROGRAMMABLE CONTROLS
+From the two examples, when the control requirements change, the diagram becomes complex, requiring more power tools (example 2). + For the programmable method, to change the program, just change the contents of the internal memory, the external wiring is not affected.
1.1 OVERVIEW OF PROGRAMMABLE CONTROLS
INS3150 - PROGRAMMING PLC

## Slide 10
Define technology requirements
Algorithm Design
Program Drafting
Load programs into memory
Test Run - Circuit Test
PLC CƠ BẢN
1.1 TỔNG QUAN VỀ ĐIỀU KHIỂN LẬP TRÌNH
PROGRAMMABLE CONTROL STEPS
1.1 OVERVIEW OF PROGRAMMABLE CONTROLS
INS3150 - PROGRAMMING PLC

## Slide 11
We just need to write a program to load into the memory of the PLC
EXAMPLE 3
Software Programming Connect the PLC to a computer with software (with driver) Transfer the program to the PLC
1
3
2
1.1 OVERVIEW OF PROGRAMMABLE CONTROLS
INS3150 - PROGRAMMING PLC
Notes: Ta cần thay đổi chương trình bên trong PLC

## Slide 12
Small size. Design changes are easier and faster when required. There is a fault diagnosis and override function. PLCs allow for maximum automation at minimal cost. Installation, programming and operation are simple. The CPUs can be used in a network, distributed system, or single use. Capable of large-scale integration. App for simple and complex controls. Less training time is required. Strong communication (PPI, Profibus-DP, AS-i)...
ADVANTAGES OF PLC
1.1 OVERVIEW OF PROGRAMMABLE CONTROLS
INS3150 - PROGRAMMING PLC

## Slide 13
In Civil:
In industry:
Small PLCs such as LOGO are used to control lighting equipment, ventilation systems, pumps, etc.
+ Elevator. + Automated production lines. + Computerization of work in production control. + Industrial robots...
ADVANTAGES OF PLC
1.1 OVERVIEW OF PROGRAMMABLE CONTROLS
INS3150 - PROGRAMMING PLC
Notes: Các PLC cỡ nhỏ như LOGO dùng để điều khiển các thiết bị chiếu sáng, hệ thống thông gió, bơm…

## Slide 14
APPLICATION OF PLC
https://www.youtube.com/watch?v=kosiOQzvZvY
1.1 OVERVIEW OF PROGRAMMABLE CONTROLS
INS3150 - PROGRAMMING PLC

## Slide 15
APPLICATION OF PLC
https://youtu.be/u2SF9QOQs6s
1.1 OVERVIEW OF PROGRAMMABLE CONTROLS
INS3150 - PROGRAMMING PLC

## Slide 16
1.2 STRUCTURE PLC
Lesson 1: PROGRAMMABLE CONTROLS
INS3150 - PROGRAMMING PLC

## Slide 17
After completing this lesson, learners will be able to: State the structure of a PLC according to the learned content. Presentation of the S7- 1200 programmable control devices. Presentation of the S7- 1200 memory structure. Handle the program exactly according to the content learned.
LESSON OBJECTIVES
INS3150 - PROGRAMMING PLC

## Slide 18
Structure of the S7-1200 program.
Structure of a PLC.
S7-1200 Programmable Control Unit.
S7-1200 Memory Structure.
Expand the in/out port.
Implement the program.
LESSON CONTENT
INS3150 - PROGRAMMING PLC

## Slide 19
LESSON CONTENT
Block source
Output
module
Memory program
CPU
Processor

Program





Input module
STRUCTURE A PLC
INS3150 - PROGRAMMING PLC

## Slide 20
1.2 STRUCTURE A PLC
Power block: the power in the PLCs is usually 24VDC, there are also PLC sets that use 220VAC power. PLCs that do not have a power module are powered externally. CPU module: (CPU: central processing unit) includes: microprocessor and memory. I/O module.
+ Input module is connected to switches, push buttons, sensors, etc. to control from an external program. + The output module is connected to the loads at the output such as the coil of the relay, contactor, signal light, optical coupler, etc.
BLOCK FUNCTIONS
INS3150 - PROGRAMMING PLC

## Slide 21
Signal transmission bus system: the signal transmission bus system consists of multiple parallel signal lines: Address bus: select addresses on different blocks. Data bus: carries data from one block to another. Control bus: transmits and transmits tensor signals and controls to synchronize operations in the PLC. The control program is loaded into memory either by a handheld programming console or by a computer. There are now a number of PLCs that are designed with keystrokes so that they can be programmed directly without the need for a handheld programmer or computer.
BLOCK FUNCTIONS
1.2 STRUCTURE A PLC
INS3150 - PROGRAMMING PLC

## Slide 22
To represent the control program on a PLC, three methods are usually used: + Ladder Diagram (LAD). + SFC (Sequential function chart) or FBD (Function Block Diagram). + List the STL (Statement List) command list.
PROGRAMMING LANGUAGES ON PLC
SFC
1.2 STRUCTURE A PLC
INS3150 - PROGRAMMING PLC

## Slide 23
This method has a similar representation to a relay contact diagram in industrial power.




K1
K1
ON
OFF
Demonstration according to mechanical contact diagram
LAD Programming Representation
X0
X1
X2
Y0
LAD PERFORMANCE METHOD
1.2 STRUCTURE A PLC
INS3150 - PROGRAMMING PLC

## Slide 24
This method represents the program as a diagram using logical ports (usually used in European notation).
SFC Representation Method
-1
&
>=1
X0
X1
X2
Y0
FBD Performance Method
SFC OR FBD PERFORMANCE
1.2 STRUCTURE A PLC
INS3150 - PROGRAMMING PLC

## Slide 25
The STL method uses evocative acronyms, similar to computer assembler language. Example:
LDI X0
LD X1
OR X2
ANB
OUT Y0
X2
X0
X1
Y0
STL PERFORMANCE METHOD
1.2 STRUCTURE A PLC
INS3150 - PROGRAMMING PLC

## Slide 26
Through the examples, we see that the three methods of representation belong to the three different fields.
The Industrial Power industry often uses the LAD method. The Electronics industry often uses the SFC or FBD method. Informatics often uses the STL method.
PLC PROGRAMMING LANGUAGE
1.2 STRUCTURE A PLC
INS3150 - PROGRAMMING PLC

## Slide 27
Working mode indicator light
Input signal indicator light
Output signal indicator light
Communication Portal
Output wiring ports
Communication of Input Modules
S7-1200 PROGRAMMABLE CONTROL UNIT
Memory Card
Power supply
1.2 STRUCTURE A PLC
INS3150 - PROGRAMMING PLC

## Slide 28
S7-1200 PROGRAMMABLE CONTROL UNIT
- 03 Compact controllers with classification in different versions like wide-range AC or DC control; - 02 Analog circuits and expansion numbers control the module directly on the CPU, reducing the product cost; - 13 different digital and analog signal modules; - 02 RS232/RS485 communication modules for communication through PTP connection; - Adding 04 Ethernet ports; - Stable PS 1207 power module, 115/230 VAC current and 24 VDC voltage
COMPONENTS PLC S7-1200 INCLUDES:
1.2 STRUCTURE A PLC
INS3150 - PROGRAMMING PLC

## Slide 29
S7-1200 PROGRAMMABLE CONTROL UNIT
COMPONENTS PLC S7-1200 INCLUDES:
1.2 STRUCTURE A PLC
INS3150 - PROGRAMMING PLC

## Slide 30
SF (red light): An SF red light indicates a system failure. RUN (green light): The RUN green light indicates that the PLC is in working mode and performs the feeding program into the machine. STOP(yellow light): The STOP yellow light indicates the PLC is in stop mode. Ix.x (green light): The green light at the entrance gate indicates the instantaneous status of port Ix.x (x.x = 0.0 to 1.5). This light signals the status of the signal according to the logical value of the gate. Qy.y (green light): The green light at the output gate signals the instantaneous status of the Qy.y gate (y.y = 0.0 to 1.1). This light signals the status of the signal according to the logical value of the gate.
DESCRIPTION OF THE INDICATOR LIGHTS ON THE S7-1200
1.2 STRUCTURE A PLC
INS3150 - PROGRAMMING PLC

## Slide 31
COMMUNICATION PORTAL S7-1200
Communicate The S7-1200 supports Profibus connection and PTP (point to point) connection. PROFINET communicates with: - Programmable Devices - HMI Equipment - Other SIMATIC controllers Supports connection protocols: - TCP/IP - SIO-on-TCP - Communication with S7
1.2 STRUCTURE A PLC
INS3150 - PROGRAMMING PLC

## Slide 32
COMMUNICATION PORTAL S7-1200
Signal Board of PLC S7-1200 Signal board – a type of module that expands in/out signals with a small number of signals, helping to save costs for applications that require small signal number expansion. Includes boards: - 1 12-bit analog output port (+- 10VDC, 0-20mA); - 2 input signal ports; - 2 signal output ports, 0.5A.
1.2 STRUCTURE A PLC
INS3150 - PROGRAMMING PLC

## Slide 33
COMMUNICATION PORTAL S7-1200
The S7-1200 has the following types of expansion modules: - Communication module (CP). - Signal board (SB) - Signal Module (SM)
1.2 STRUCTURE A PLC
INS3150 - PROGRAMMING PLC

## Slide 34
Program
Parameter
Object
EEPROM
Program
Parameter
Object
External memory domains
Program
Parameter
Data
Object
Capacitor
S7-1200 MEMORY STRUCTURE
1.2 STRUCTURE A PLC
INS3150 - PROGRAMMING PLC

## Slide 35
Program Region: This is the memory domain used to store program commands. Read/write area. Parameter area: It is the domain that stores parameters such as keywords, temporary addresses, etc. Read/write area. Data region: Stores data such as the results of calculations, constants defined in the program, media buffers, etc. Read/write zone. Object Area: Timer, counter, high-speed counter, analog I/O ports. Read/write area. The last two memory areas are important, which are detailed in the following section.
DIVIDING MEMORIES:
1.2 STRUCTURE A PLC
INS3150 - PROGRAMMING PLC

## Slide 36
A data region is a dynamic memory region. Accessed bit-by-bit, byte-byte, single word or double word. Used as a data storage domain for algorithms, communication functions, tabling, shift functions, record rotating, address pointers. Data area are divided into small memory domains with different uses. They are denoted as follows:
+ V : Variable memory.
+ I : Input image register.
+ O : Output image register
+ M : Internal memory bits.
+ SM : Special memory bits.
DATA AREA:
1.2 STRUCTURE A PLC
INS3150 - PROGRAMMING PLC

## Slide 37
CPU OBJECT PARTITIONING
CPU S7-1200
1.2 STRUCTURE A PLC
INS3150 - PROGRAMMING PLC

## Slide 38
The I/O port of the PLC can be expanded by adding to it the expansion modules towards the right side of the CPU, forming a chain. The address of the position of the module is determined by the input/exit type and of the module in the chain hook including the module of the same type. For example, an output module cannot be assigned the address of an input module, just as an analog module cannot be addressed as a number module, and vice versa. Digital or similar modules all occupy space in the buffer corresponding to the number of inputs/outputs of the module.
EXPANDING THE CPU IN AND OUT
1.2 STRUCTURE A PLC
INS3150 - PROGRAMMING PLC

## Slide 39
I0.0
I0.1
I0.2
I0.3
I0.4
I0.5
I0.6
I0.7
I1.0
I1.1
I1.5
Q0.0
Q0.1
Q0.2
Q0.3
Q0.4
Q0.5
Q0.6
Q0.7
Q1.0
Q1.1
…
CPU
I2.0
I2.1
I2.2
I2.3
Q2.0
Q2.1
Q2.2
Q2.3
Module 0
4vào/4ra
I3.0
I3.1
I3.2
I3.3
I3.4
I3.5
I3.6
I3.7
Module 1
8 vào
AIW0
AIW2
AIW4
AQW0
Module 2
3vào/ 1ra
Q3.0
Q3.1
Q3.2
Q3.3
Q3.4
Q3.5
Q3.6
Q3.7
Module 3
8 ra
AIW8
AIW10
AIW12
AQW4
Module 4
3vào/ 1ra
EXPANDING CPU IN/OUT PORTS
1.2 STRUCTURE A PLC
INS3150 - PROGRAMMING PLC

## Slide 40
EXPANDING CPU IN/OUT PORTS
1.2 STRUCTURE A PLC
INS3150 - PROGRAMMING PLC

## Slide 41
The PLC performs the program in a repeating cycle. Each loop is called a scan loop.
PLC scan cycle
1/ Entering the periphery into the virtual cache
2/ Implementation of the program
3/ Communication and error self-testing
4/ Transfer data from the virtual cache to the offsite
PROGRAM IMPLEMENTATION
1.2 STRUCTURE A PLC
INS3150 - PROGRAMMING PLC

## Slide 42
Each scan round is started with: The stage reads data from the ports into the virtual buffer. Program implementation stage. Internal communication and debugging phase. The scan round ends with the phase of transferring the contents of the virtual buffer to the output ports.
PROGRAM IMPLEMENTATION
SEND SIGNAL TO OUTPUT
RECEIVING SIGNALS FROM INPUTS
PROGRAM IMPLEMENTATION
MEDIA HANDLING
CPU STATUS CHECK
PLC Scan Cycle
1.2 STRUCTURE A PLC
INS3150 - PROGRAMMING PLC

## Slide 43
In each scan, the program is executed with the first command and ends at the end command.
When encountering an entry/exit order, the system will immediately stop all other work, even the interrupt processing program, to execute the command directly with the entry/exit port.
PROGRAM IMPLEMENTATION
SEND SIGNAL TO OUTPUT
RECEIVING SIGNALS FROM INPUTS
PROGRAM IMPLEMENTATION
MEDIA HANDLING
CPU STATUS CHECK
PLC Scan Cycle
1.2 STRUCTURE A PLC
INS3150 - PROGRAMMING PLC

## Slide 44
SBR n
(Subprogramsn+1)
RET
…
INT n
(Interrupt Programn+1)
RETI
…
Main Program
END
…
(Perform in one scan)
Perform when called by the main program
Perform when there is an interrupt signal
SBR 0 (Subprograms1)
RET
…
INT 0 (Interrupt Program1)
RETI
…
S7-1200 PROGRAM STRUCTURE
1.2 STRUCTURE A PLC
INS3150 - PROGRAMMING PLC

## Slide 45
The main program is locked with the END command. The subprogram is a part of the program. Finish with the RET command and write after the main program. The interrupt processing program is a part of the program. Finish with the RETI command and write after the main program.
PROGRAM STRUCTURE
1.2 STRUCTURE A PLC
INS3150 - PROGRAMMING PLC

## Slide 46
The subprograms are grouped into a group after the main program. Then immediately come to the interrupt processing programs. It is possible to freely confuse subprograms and interrupt processing programs behind the main program. The software used for the PLC S7-1200 is TIA PORTAL.
PROGRAM STRUCTURE
1.2 STRUCTURE A PLC
INS3150 - PROGRAMMING PLC